## Slide 1
Internet of Things - Introduction

## Slide 2: Module Aims
The main aim of this module is to introduce the fundamental concepts of the Internet of Things and its applications and architecture models;
Introduction to the technologies and mechanisms for sensing, actuation, processing and cyber-physical data communication.
Discussing semantic technologies, service oriented solutions and networking technologies that enable the integration of Internet of Things data and services into the cyber world (i.e. the Internet and the Web).
To develop practical skills that can be transferred into a real-world environment.

## Slide 3
IBM Mainframe 360, source Wikipedia

## Slide 4
Apollo 11 Command Module (1965) had 64 kilobytes of memory
operated at 0.043MHz.
An iPhone 5s has a CPU running at speeds of up to 1.3GHz
and has 512MB to 1GB of memory
Cray-1 (1975) produced 80 million Floating point operations per second (FLOPS)
10 years later, Cray-2 produced 1.9G FLOPS
An iPhone 5s produces 76.8 GFLOPS – nearly a thousand times more
Cray-2 used 200-kilowatt power
Source: Nick T., PhoneArena.com, 2014

## Slide 5: Computing Power
Smaller size
More Powerful
More memory and more storage
"Moore's law" over the history of computing, the number of transistors in a dense integrated circuit has doubled approximately every two years.

## Slide 6: Cyber-Physical-Social Data
P. Barnaghi et al., "Digital Technology Adoption in the Smart Built Environment", IET Sector Technical Briefing, The Institution of Engineering and Technology (IET), I. Borthwick (editor), March 2015.

## Slide 8: Sensor devices are becoming widely available
- Programmable devices
- Off-the-shelf gadgets/tools

## Slide 9: More “Things” are being connected
Home/daily-life devices
Business and
Public infrastructure
Health-care
…

## Slide 10: People Connecting to Things
Motion sensor
Motion sensor
Motion sensor
ECG sensor
Internet

## Slide 11: Things Connecting to Things
- Complex and heterogeneous
resources and networks

## Slide 12: Wireless Sensor Networks (WSN)
Sink
node
Gateway
Core network
e.g. Internet
Gateway
End-user
Computer services
The networks typically run Low Power Devices
Consist of one or more sensors, could be different type of sensors (or actuators)

## Slide 13: How are the networks changing?
Extensions
  More nodes, more connections
  Any TIME, Any PLACE + Any THING
  M2M, IoT
    Billions of interconnected devices,
    Everybody is connected.
Expansions
  Broadband
  LTE, 5G
Enhancements
  Smart networks
  Data-centric and content-oriented networking
  Context-aware (autonomous) systems

## Slide 14: “Thing” connected to the internet
Source: CISCO

## Slide 15: Internet of Things (IoT)
Extending the current Internet and providing connection, communication, and inter-networking between devices and physical objects, or "Things," is a growing trend that is often referred to as the Internet of Things.
“The technologies and solutions that enable integration of real world data and services into the current information networking technologies are often described under the umbrella term of the Internet of Things (IoT)”

## Slide 16
From any time ,any place connectivity for anyone, we will now
have connectivity for anything!

## Slide 17: Why should I learn about IoT?
Emerging technologies
Growing IoT Services and Applications in various areas including smart cities, healthcare, transport, logistics, retail, safety and security, etc.
Business trends and new opportunities

## Slide 18: Opportunities
Source: http://blog.trentonsystems.com/internet-of-things-crosses-business-personal-boundaries/

## Slide 19: History of IoT
1997, “The Internet of Things” is the seventh in the series of ITU Internet
Reports originally launched in 1997 under the title “Challenges to the Network”
1999, Auto-ID Center founded in MIT
2003, EPC Global founded in MIT
2005, Four important technologies of the internet of things was
proposed in WSIS conference, nano tech, wireless sensor, RFID and smart tech
2008, First international conference of internet of things: The IOT 2008 was held at Zurich

## Slide 20: Technology trend

## Slide 21: Smart product sales
Source: Siemens, http://www.siemens.com/innovation/apps/pof_microsite/_pof-fall-2012/_html_en/facts-and-forecasts-growth-market-of-the-future.html

## Slide 22: Internet Connected devices
Source: Siemens, http://www.siemens.com/innovation/apps/pof_microsite/_pof-fall-2012/_html_en/facts-and-forecasts-growth-market-of-the-future.html

## Slide 23: Global Data Generation
Everyday around 20 quintillion (10^18) bytes of data are produced (Source: http://www-01.ibm.com/software/data/bigdata/).
- This data includes textual content (unstructured, semi-structured, structured) to multimedia content (images, video and audio), on a variety of platforms (enterprise, social media, and sensors).

## Slide 24: Data Generation

## Slide 25: Data Lifecycle
Source: The IET Technical Report, Digital Technology Adoption in the Smart Built Environment: Challenges and opportunities of data driven systems for building, community and city-scale applications, http://www.theiet.org/sectors/built-environment/resources/digital-technology.cfm

## Slide 26
“The ultimate goal is transforming the raw data to insights and actionable knowledge and/or creating effective representation forms for machines and also human users and creating automation.”
This usually requires data from multiple sources, (near-) real time analytics and visualisation and/or semantic representations.

## Slide 27: Internet of Things
P. Barnaghi, A. Sheth, “Internet of Things, The story so far”, IEEE IoT Newsletter, September 2014.

## Slide 28: Internet of Things Module
Image courtesy: Wilgengebroed

## Slide 29: Topics
Cyber-Physical systems, smart devices, sensors and actuators
Key applications, protocols and architectures
Networks and Communications (Wireless Multi-hop Networks (WMN), Mobile Ad-hoc Networks (MANET), Wireless Sensor Networks (WSN))
Reliability, Security, Privacy and Trust issues and solutions
Software platforms and services
Intelligent Data Processing and Semantic technologies
Connecting Things to the Web (Web of Things)
Applications, system models, Standards, and Physical-Cyber-Social systems (invited industry speaker?)

## Slide 30: Module Web Link
All the slides and additional material will be uploaded to SurreyLearn
  http://surrylearn.surrey.ac.uk

## Slide 31: Some of the related material
Reading List:
  http://aspire.surrey.ac.uk/lists/35640FC8-892D-E309-E66C-F07C3D9BCB28.html

## Slide 32: IoT Architecture
Three major components for designing any IoT system
Application devices: Hardware architecture, smart sensors, cloud computing, energy efficient devices
Networks: Communication technology, advanced internet protocol, wireless technology, RFID technology
Security and privacy: Authentication procedure, secure device discovery, secure inter-device communication

## Slide 33: Overview: Hardware Platform
The Internet
Network
“Thing”
Sensors & Actuators
Communications
User/Environment
Servers
2 sensors
IEEE 802.15.4 2.4GHz RF System
XM1000
Device level
Network level
The Internet
Gateway

## Slide 34: Sensors & Actuators
Sensors:
  They are mainly input components
  They sense and collect surrounding information
  Basically three types:
    Passive, omnidirectional (e.g. mic)
    Passive, narrow-beam sensor (e.g. PIR)
    Active sensors (e.g. sonar, radar, etc.)
Actuators:
  They are mainly output components
  They alter the surrounding. Some examples:
    Adding lighting, heat, sound, etc.
    Controlling motors to move objects
    Displaying messages
    and others…

## Slide 35: Things
We can turn almost every object into a “thing”.
A “thing” still looks much like an embedded system currently.
A “thing” generally consists of four main parts:
  Sensors & actuators
  Microcontroller
  Communication unit
  Power supply
A “thing” has the following properties:
  It’s usually powered by battery. This implies limited source of energy.
  It’s generally small in size and low in cost. This limits their computing capability.
  It doesn’t usually perform complicated tasks.
Power consumption is the main design issue.

## Slide 36: Communications
A “thing” always feature communications for “team working”
The Role of Communications
  Providing a data link between two nodes
Communication type:
  Wireline (e.g. copper wires, optical fibers)
  Wireless (e.g. RF, IR). RF-based communication is the most popular choice (and also our focus)
Popular RF-based communication solutions:
  IEEE 802.15.4  used in XM1000
  IEEE 802.11 (or Wifi)
  Bluetooth
  Near Field Communication (NFC), e.g. RFID

## Slide 37: Networks
The Roles of Networks
  Managing nodes (discovery, join, leave, etc).
  Relaying data packets from the source to the destination node in the network.
Networks are a distributed system. All nodes need to perform networking related tasks.
RF-based Network in IoT is usually a Wireless Multi-hop Network. Some examples:
  Wireless Sensor Networks (WSNs)
  Mobile Wireless Ad hoc Networks (MANETs)
  Wireless Mesh Networks (WMNs)
  Vehicular Ad Hoc Networks (VANETs)
  and others...
Main concern: Reliability & Performance

## Slide 38: The Internet
The Internet serves as a wide area networking for a local network.
The Internet uses TCP/IP. This implies that things must also support TCP/IP.
Gateway (or sink)
  For a practical deployment, a gateway is often needed in a network.
  It offers relaying packets between the network and the Internet.
The Internet
Gateway
Data link
Network

## Slide 39: Protocol Stack
Network (IP)
IEEE 802.15.4 PHY/MAC
TCP/UDP
Application
Network (IP)
IEEE 802.15.4 PHY/MAC
TCP/UDP
Application
IEEE 802.15.4 PHY/MAC
Network (IP)
IEEE 802.3 (Ethernet)
Network (IP)
IEEE 802.3 (Ethernet)
TCP/UDP
Application
Wireless Medium
The Internet
Thing
Thing
Gateway
Server

## Slide 40: Security & Privacy
Are they important?
What is the risk?
What are the challenges?
  Device level
  Network level
  System level
  User level
Solutions?

## Slide 41: Software Platforms and Services
Operating Systems and execution environments
  Contiki, TinyOS
Relevant protocols and standards
  6LoWPan, CoAP
Architecture reference models
ETSI M2M architecture and components
Gateway/middleware
Types of services
  In conventional communication networks the target is moving bits from one place to another
  In the IoT moving the data is not the actual goal.
    The IoT is expected to facilitate providing meaningful information/actions.

## Slide 42: Example: Type of Services in IoT
Sink
node
Gateway
Core network
e.g. Internet
End-user
Data
Sender
Data
Receiver
A sample data communication in conventional networks
A sample data communication in WSN
Fire!
Some bits
01100011100

## Slide 43: Intelligent Data Processing
Sensing and data collection, sensor data and data-centric networks
Access, subscription and integration
Data processing and stream data analysis
Query and discovery
Data classification and clustering

## Slide 44: Things, Data, and lots of it
image courtesy: Smarter Data - I.03_C by Gwen Vanhee

## Slide 45
“Each single data item is important.”
“Relying merely on data from sources that are unevenly distributed, without considering background information or social context, can lead to imbalanced interpretations and decisions.”
?

## Slide 46: IoT Data- Challenges
Multi-modal and heterogeneous
Noisy and incomplete
Time and location dependent
Dynamic and varies in quality
Crowed sourced data can be unreliable
Requires (near-) real-time analysis
Privacy and security are important issues
Data can be biased- we need to know our data!

## Slide 47
“People want answers, not numbers” (Steven Glaser, UC Berkley)
Sink
node
Gateway
Core network
e.g. Internet
What is the temperature at home?
Freezing!

## Slide 48: Storing, Handling and Processing the Data
Image courtesy: IEEE Spectrum

## Slide 49: Semantic technologies and connecting Things to the Web
Meta-data models and schemas
Linked data and Linked IoT data concepts
Semantic technologies and semantic sensor networks
Interoperability issues
Web of Things

## Slide 50: Device/Data interoperability
The slide adapted from the IoT talk given by Jan Holler of Ericsson at IoT Week 2015 in Lisbon.

## Slide 51: Observation and measurement data
Source: W3C Semantic Sensor Networks, SSN Ontology presentation, Laurent Lefort et al.

## Slide 52: System models, Applications and Standards
Applications: Smart City, Smart Homes, Healthcare, Smart Grid,
Physical-Cyber-Social Systems
Machine-to-machine communications
System models and Standards

## Slide 54: Questions?