## Slide 1: An Overview of the Aloha protocols

## Slide 2: History
One of the early computer networking designs
Developed at the U of Hawaii in 1970 under the leadership of N Abramson.
Wanted to create a wireless network that would allow remote UH campuses to access centrally-located computing resources

## Slide 3: Basic design
Original version used hub/star topology
  Hub computer broadcasted packets to everyone on an outbound channel
  Client machines sent data to the hub on a shared inbound channel

## Slide 4: Handling contention
Client machines transmit without knowing whether another clients transmit at the same
  No reservations
  No time-domain multiplexing
Cannot either detect collisions
  Their own signal always overpowers signals from other clients

## Slide 5: The solution
Hub site immediately retransmits the packets it has received on its broadcast channel
Any client noticing one of its packets was not acknowledged
  Waits a short time
  Retransmits the packet

## Slide 6: Aloha and Ethernet (I)
Aloha predates Ethernet by several years
Like Aloha
  Ethernet clients share a single contention channel
  Retransmits packets that were damaged due to a collision

## Slide 7: Aloha and Ethernet (II)
Unlike Aloha
  Ethernet clients sense the network before transmitting a packet
  Abort packet transmission as soon as they detect a collision
  Both options are not possible on a packet radio network

## Slide 8: A concise view of the protocol
If you have data to send, send the data
If the message collides with another transmission, try resending "later"
http://en.wikipedia.org/wiki/ALOHAnet

## Slide 9: Analysis (I)
Let d be the duration of a packet transmission interval
Let G the average number of packets transmitted per transmission interval
  Including retransmissions
A packet will collide with any packet sent
  Less than d time units before it was transmitted
  While it was transmitted

## Slide 10: The “danger zone”
Colliding packet
Packet being sent
Colliding packet
2d

## Slide 11: The results
Throughput S
  = G Prob[successful transmission]
  = G Prob[no collision]
  = G Prob[no other transmission within 2d]
  = G exp(-2G)
Reaches maximum for G = 0.5
  Maximum throughput is 18.4% of bandwidth

## Slide 12: Slotted Aloha
(Roberts 1972)
Divides time into fixed-size slots
  Slot sizes is equals to packet transmission time
Clients must wait until start of next slot before sending a packet
  Packets either overlap completely or not at all
  Danger zone is duration of a slot

## Slide 13: The “danger zone” for slotted Aloha
Packet being sent
Colliding packet
d
Packet being sent
Packet being sent
Slot
Slot
Slot

## Slide 14: Analysis
Throughput S
  = G Prob[successful transmission]
  = G Prob[no collision]
  = G Prob[no other transmission within slot]
  = G exp(-G)
Reaches maximum for G = 1
  Maximum throughput is 36.8% of bandwidth

## Slide 15: Finite-population slotted Aloha
Let Gi be the total transmission rate of user i for i = 1, 2, …, N in number of packets per slot
Let Si be the number of new packets generated by user i during a given slot.
Gi is also the probability that user i transmits a packet during a slot.

## Slide 16: Finite-population slotted Aloha
We have
  Si = Gi Πi ≠ j (1 – Gj)
If Si = S/N and Gi = G/N
  S = G [1 – G/N ]N-1
and
  limN->∞ S = G [1 – G/N ]N-1 = exp(-G)

## Slide 17: Implementation details
Clients never schedule the transmission of a new packet before the previous packet has been correctly received by the hub site
  Each client maintains a queue of packets ready for transmission and transmits them one by one

## Slide 18: Frame Slotted ALOHA
The ALOHA algorithm is a collision resolution algorithm based on Time Division Multiple Access (TDMA).
There are three flavors of the original ALOHA algorithm:
  (Pure) ALOHA,
  SlottedALOHA and
  FrameSlotted ALOHA

## Slide 20
The read cycle is divided into discrete time intervals called slotand which is synchronized with the entire tags by the reader. Thus, tags must choose one of the slots randomly and transmit data within a single slot. Transmission begins right after a slot delimiter. This causes that packets either collide completely or don’t collide at all i.e. there is no partial collision in the Slotted ALOHA algorithm.

## Slide 21
This reduces wasting the read cycle relatively as compared with the (Pure) ALOHA algorithm.
However, the empty slot can be occurred in the read cycle and the disadvantage is that it requires a synchronization mechanism in order for the slot-begin to occur simultaneously at all tags.

## Slide 22: Framed slotted ALOHA
Framed SlottedALOHA algorithm uses the frame which is the discrete time interval of the read cycle and each frame is divided into the same number of slots.
There are multiple frames in a single read cycle and the frame size is decided by the reader (Figure 3)
There is a constraint that the tags can transmit data only once in each frame. It may reduce the number of collided slots and it shows the best performance among them.

## Slide 23: Framed Slotted ALOHA Algorithms