## Slide 1: Internet of Everything (IoE)
Dr. Vinayak Ashok Bharadi

## Slide 2: Sensors
What are the sensors?
Sensor Family
Architecture of a Single Node Sensor.

## Slide 3: Sensors
Sensors are sophisticated devices that are frequently used to detect and respond to electrical or optical signals. A Sensor converts the physical parameter (for example: temperature, blood pressure, humidity, speed, etc.) into a signal which can be measured electrically.
In the broadest definition, a sensor is a device, module, machine, or subsystem whose purpose is to detect events or changes in its environment and send the information to other electronics, frequently a computer processor. A sensor is always used with other electronics.

## Slide 5: Criteria to choose a Sensor
1. Accuracy
2. Environmental condition – usually has limits for temperature/ humidity
3. Range – Measurement limit of sensor
4. Calibration – Essential for most of the measuring devices as the readings changes with time
5. Resolution – Smallest increment detected by the sensor
6. Cost
7. Repeatability – The reading that varies is repeatedly measured under the same environment

## Slide 6: Classification of Sensors
The sensors are classified into the following criteria:
1. Primary Input quantity (Measurand)
2. Transduction principles (Using physical and chemical effects)
3. Material and Technology
4. Property
5. Application

## Slide 7: Classification based on property is as given below:
Temperature – Thermistors, thermocouples, RTD’s, IC and many more.
Pressure – Fibre optic, vacuum, elastic liquid based manometers, LVDT, electronic.
Flow – Electromagnetic, differential pressure, positional displacement, thermal mass, etc.
Level Sensors – Differential pressure, ultrasonic radio frequency, radar, thermal displacement, etc.
Proximity and displacement – LVDT, photoelectric, capacitive, magnetic, ultrasonic.

## Slide 8
Biosensors – Resonant mirror, electrochemical, surface Plasmon resonance, Light addressable potentio-metric.
Image – Charge coupled devices, CMOS
Gas and chemical – Semiconductor, Infrared, Conductance, Electrochemical.
Acceleration – Gyroscopes, Accelerometers.
Others – Moisture, humidity sensor, Speed sensor, mass, Tilt sensor, force, viscosity.

## Slide 9: Classification based on Application is as given below:
Industrial process control, measurement and automation
Non-industrial use – Aircraft, Medical products, Automobiles, Consumer electronics, other type of sensors

## Slide 10: Sensors can be classified based on power or energy supply requirement of the sensors:
Active Sensor – Sensors that require power supply are called as Active Sensors. Example: LiDAR (Light detection and ranging), photoconductive cell.
Passive Sensor – Sensors that do not require power supply are called as Passive Sensors. Example: Radiometers, film photography.

## Slide 11: In the current and future applications, sensors can be classified into groups as follows:
Accelerometers – These are based on the Micro Electro Mechanical sensor technology. They are used for patient monitoring which includes pace makers and vehicle dynamic systems.
Biosensors – These are based on the electrochemical technology. They are used for food testing, medical care device, water testing, and biological warfare agent detection.
Image Sensors – These are based on the CMOS technology. They are used in consumer electronics, biometrics, traffic and security surveillance and PC imaging.
Motion Detectors – These are based on the Infra Red, Ultrasonic, and Microwave / radar technology. They are used in videogames and simulations, light activation and security detection.

## Slide 17: Wireless Sensor Node

## Slide 18: References
https://www.engineersgarage.com/article_page/sensors-different-types-of-sensors/